## Slide 1: Constant Value Prediction
Prajyot Gupta, Satvik Maurya, and Robert Viramontes
CS/ECE 752 Spring 2021

## Slide 2: Constant Value Prediction
Background
Implementation
Results
Future Work

## Slide 3: Background
“Value Locality and Load Value Prediction”, M. Lipasti et al described value locality and mechanism to exploit it in ASPLOS’96.
  Value locality when a storage location’s value is stable
Motivation
  Speculation on stable values
  Skip memory accesses on very stable values
Examine the technique under newer benchmarks
Notes: Our Project is based on Professor Mikko’s work on “Value Locality and Load VP”, in ASPLOS’ 96.
The credo of our work is based on the concept of value locality: value locality describes the likelihood of the recurrence of a previously-seen value within a storage location.
Drawing a parallel from Branch Prediction – eliminates the control dependences  Value Prediction – eliminates the data dependences
The main intent of VP is to predict the results of a load operation based on previously occurring loads.
The Load prediction is performed during the Fetch and Decode stages of the pipeline. Thus, the dependent instructions can be issued immediately.
Why Load value prediction and not store value predition? - Praj
A store op, that updates a base register is quite unlikely to exhibit any sort of locality. On the other hand, a load is very likely to have both spatial and temporal locality because any value stored in memory will likely be accessed more than once. Thus, Lipasti here focuses on VP for Load instructions.

## Slide 4: Constant Value Prediction
Background
Implementation
Results
Future Work

## Slide 5: Implementation – Load Value Prediction Unit
Prediction Value
Implemented a single LVP unit to coordinate logic between
  Load Classification Table (LCT)
  Load Value Prediction Table (LVPT)
  Constant Verification Unit (CVU)
Classifies loads as Unpredictable, Predictable, or Constant
Index | Prediction Strength
Index | Prediction Value | Valid
Data Address | Index
LCT
LVPT
CVU
PC
Addr
Notes: In the implementation of LVP, we used three blocks:
Load Value Prediction Table (LVPT): The LVPT stores the predicted values to be used for later instructions. It is a cache that is indexed by the instruction address and uses the standard LRU replacement mechanism. It is direct-mapped, untagged so that constructive and destructive interference can occur between loads that map to the same entry
Load Classification Table (LCT): The LCT is used to answer the question of when predictions should be made. Again, the table is indexed by the instruction address, but now instead of storing a value, the table stores a saturating counter that keeps track of how predictable the instruction is.
--- work on this

## Slide 6: Implementation – CPU Modifications
Minor
Fetch 1
Fetch 2
Decode
LVPU
LSQ
GetPrediction
Req
Resp
Const. Load
Store
VerifyPrediction
Issue
Execute
Commit
DerivO3
Fetch
Decode
Rename
I/E/W
LVPU
LSQ
GetPrediction
Req
Resp
Const. Load
Store
VerifyPrediction
Dispatch
Notes: Robert
In the minor, we modify the decode stage to tag the dynamic instruction with the load classification and the load value from the LCT and LVPT.
In the commit phase, memory accesses are sent to the LSQ. At the LSQ, for constant loads we check with the CVU to verify that the load can proceed as constant. If it can proceed as constant, the response packet updated with the predicted value and the response is returned without touching the memory hierarchy. All stores are also sent to the CVU to invalidate any matching data addresses to stay coherent with main memory.
Finally, all load instructions that reach commit are sent to the LVP where they strengthen the prediction of LCT and update value of LVPT.

## Slide 7: Constant Value Prediction
Background
Implementation
Results
Future Work

## Slide 8: Results: Gem5 Simulation Configurations
Variation of LVP | Configuration |  | 
 | LCT | LVPT | CVU
Baseline - w/o LVP | n/a | n/a | n/a
Variation-0 (LVP Baseline) | 512 entries, 2-bit counter | 1024 entries, history depth of 1 | 8 entries/thread, FIFO replacement policy
Variation-1 | 512 entries, 4-bit counter | 1024 entries, history depth of 1 | 8 entries/thread, FIFO replacement policy
Variation-2 | 1024 entries, 2-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, FIFO replacement policy
Variation-3 | 1024 entries, 2-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, LRU replacement policy
Variation-4 | 1024 entries, 2-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, NLRU replacement policy
Variation-5 | 1024 entries, 2-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, MRU replacement policy
Variation-6 | 1024 entries, 2-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, NMRU replacement policy
Variation-7 | 1024 entries, 4-bit counter | 4096 entries, history depth of 16 | 32 entries/thread, FIFO replacement policy
Notes: Prajyot
When running our benchmarks, we use 8 variations of the LVP unit to understand the effects of different parameters on the impact of the LVPU. Key parameters include # LCT entries, counter size for LCT, # LVPT entries, LVPT history depth, CVU entries/thread, and CVU replacement policy. V0, V1,V2, and V7 allow us to view the impact of various hardware changes. V2-V6 form more or less “ideal” hardware that allow us to view the impact of CVU replacement policy.
Varying entry sizes
2 vs 4-bit counter
Varying replacement policies

## Slide 9: Results – Minor CPU
Min: 0.2836, Max: 99.90
Chart: Constant Coverage %
| bzip2 | libquantum | sjeng
LVP_V0 | 18.116 | 33.3402 | 1.1695
LVP_V1 | 16.5004 | 16.6694 | 1.0225
LVP_V2 | 16.5682 | 16.6705 | 1.3013
LVP_V3 | 16.6438 | 16.6705 | 1.3609
LVP_V4 | 16.5649 | 16.6705 | 1.2981
LVP_V5 | 10.3976 | 16.6705 | 0.81891
LVP_V6 | 16.5687 | 16.6705 | 1.3008
LVP_V7 | 15.8362 | 16.6694 | 1.1584
Min: 0.1898, Max: 33.34
Chart: Constant Accuracy %
| bzip2 | libquantum | sjeng
LVP_V0 | 51.7149 | 49.9498 | 55.3565
LVP_V1 | 56.7833 | 99.9024 | 59.1577
LVP_V2 | 59.1618 | 99.8975 | 68.9045
LVP_V3 | 59.214 | 99.8975 | 71.9075
LVP_V4 | 59.1557 | 99.8975 | 68.5619
LVP_V5 | 12.9835 | 99.8974 | 0.28359
LVP_V6 | 59.1664 | 99.8975 | 68.7952
LVP_V7 | 61.1104 | 99.9024 | 72.0679
Notes: Robert
Two of the key metrics we want to look at are the coverage and the accuracy of the constant predictions, as defined by Seznec in their work with value prediction. The coverage indicates the total number of loads that were tagged in decode as constant. The accuracy is the % of constant predictions that were correct and executed in LSQ as constant. Important to note that the total number of constants executed as constants is a function of both of these numbers.
Here, we see that the libquantum benchmark exhibits strong value locality, with relatively high coverage and very high accuracy (100%). We also note, particularly obvious in libquantum, that there is a tradeoff between coverage and accuracy because there is, overall, a fixed number of loads that are constant. We also see, compared to

## Slide 10: Results – Minor CPU
Chart: IPC, Normalized to Unmodified Minor
| bzip2 | libquantum | sjeng
Baseline | 1 | 1 | 1
LVP_V0 | 1.0051 | 1.0057 | 1.0002
LVP_V1 | 1.0051 | 1.0057 | 1.0001
LVP_V2 | 1.0067 | 1.0057 | 1.0001
LVP_V3 | 1.0067 | 1.0057 | 1.0002
LVP_V4 | 1.0067 | 1.0057 | 1.0001
LVP_V5 | 0.99937 | 1.0057 | 1
LVP_V6 | 1.0067 | 1.0057 | 1.0001
LVP_V7 | 1.0052 | 1.0057 | 1.0001
Chart: D$ Accesses, Normalized to Unmodified Minor
| bzip2 | libquantum | sjeng
Baseline | 1 | 1 | 1
LVP_V0 | 0.86201 | 0.50031 | 0.99833
LVP_V1 | 0.86193 | 0.50031 | 0.99844
LVP_V2 | 0.85571 | 0.50031 | 0.99769
LVP_V3 | 0.85492 | 0.50031 | 0.99748
LVP_V4 | 0.85575 | 0.50031 | 0.99771
LVP_V5 | 0.9801 | 0.50031 | 0.99999
LVP_V6 | 0.85569 | 0.50031 | 0.99769
LVP_V7 | 0.85739 | 0.50031 | 0.99785
Min: 0.9994, Max: 1.007
Min: 0.5003, Max: 1.000
12,358,095
5,000,446
22,229,646
Notes: Robert
Here, we plot the IPC and D$ accesses, normalized to the baseline (which is included). IPC is hardly affect, which we’ll discuss more in our summary.
The D$ accesses provide some more interesting results. In benchmarks that exhibit strong constant values like libquantum, we are able to significantly reduce D$ accesses by almost half even with the smallest version of the hardware (v0). This also corroborates the discussion from the previous slide about the coverage and accuracy, as we can see the reduction of the D$ is approximately the same for libquantum for all variations even though there were significant variations in the coverage/accuracy.

## Slide 11: Results – DerivO3 CPU
Chart: Coverage for Constant Load Predictions
| bzip2 | specrand | libquantum | sjeng
LVP_V0 | 0.043871 | 0.23143 | 0.49806 | 0.18927
LVP_V1 | 0.025129 | 0.21195 | 0.49796 | 0.13278
LVP_V2 | 0.045155 | 0.26721 | 0.49805 | 0.1891
LVP_V3 | 0.045771 | 0.26721 | 0.49805 | 0.18902
LVP_V4 | 0.045133 | 0.26717 | 0.49805 | 0.18909
LVP_V5 | 0.039803 | 0.2404 | 0.49805 | 0.18567
LVP_V6 | 0.043906 | 0.26721 | 0.49806 | 0.18927
LVP_V7 | 0.026215 | 0.25639 | 0.498 | 0.1343
Chart: Accuracy for Constant Load Predictions
| bzip2 | specrand | libquantum | sjeng
LVP_V0 | 0.47675 | 0.33393 | 0.99992 | 0.51803
LVP_V1 | 0.81023 | 0.35631 | 1 | 0.53805
LVP_V2 | 0.54701 | 0.31871 | 0.99994 | 0.57108
LVP_V3 | 0.57808 | 0.31873 | 0.99994 | 0.58664
LVP_V4 | 0.54567 | 0.31835 | 0.99994 | 0.57038
LVP_V5 | 0.24067 | 0.011908 | 0.99991 | 0.029017
LVP_V6 | 0.47764 | 0.31871 | 0.99992 | 0.51634
LVP_V7 | 0.89546 | 0.32008 | 1 | 0.5593
Notes: Satvik

## Slide 12: Results – DerivO3 CPU
Chart: IPC Value
| bzip2 | specrand | libquantum | sjeng
Baseline | 1 | 1 | 1 | 1
LVP_V0 | 1.0012 | 1.0008 | 1.0103 | 1
LVP_V1 | 1.0012 | 1.0007 | 1.0103 | 1
LVP_V2 | 1.0012 | 1.0008 | 1.0103 | 1
LVP_V3 | 1.0012 | 1.0008 | 1.0103 | 1
LVP_V4 | 1.0012 | 1.0008 | 1.0103 | 1
LVP_V5 | 1.0004 | 1 | 1.0103 | 1
LVP_V6 | 1.0012 | 1.0008 | 1.0103 | 1
LVP_V7 | 1.0012 | 1.0008 | 1.0103 | 1
Chart: D$ Accesses, Normalized to Unmodified Baseline
| bzip2 | specrand | libquantum | sjeng
Baseline | 1 | 1 | 1 | 1
LVP_V0 | 0.97948 | 0.94943 | 0.74909 | 0.99927
LVP_V1 | 1 | 0.95063 | 0.74912 | 0.99947
LVP_V2 | 0.97948 | 0.94912 | 0.74909 | 0.99919
LVP_V3 | 1 | 0.94912 | 0.74909 | 0.99917
LVP_V4 | 0.97948 | 0.94919 | 0.74909 | 0.9992
LVP_V5 | 1 | 1 | 0.7491 | 0.99996
LVP_V6 | 0.97948 | 0.94943 | 0.74909 | 0.99927
LVP_V7 | 1 | 0.95063 | 0.7491 | 0.99944
Notes: Satvik

## Slide 13: Results – Summary
Very slight impact on IPC
  Can be attributed to the fact that almost ALL constant loads were L1D$ residents.
  Constant load forwarding was very conservative.
For certain workloads, constant locality offers promising opportunity to reduce cache accesses
Design space exploration by increasing # entries had marginal effect on accuracies, can keep relatively small + cheap
Block replacement policy for the CVU CAM important!
Notes: Satvik

## Slide 14: Constant Value Prediction
Background
Implementation
Results
Future Work
Notes: Satvik

## Slide 15: Future Work
Optimized/aggressive constant forwarding
Predictable forwarding and squashing of results
CMP - Cache coherence complications
Notes: Satvik

## Slide 16: Backup

## Slide 17: References
Lipasti, Mikko H., Christopher B. Wilkerson, and John Paul Shen. "Value locality and load value prediction." Proceedings of the seventh international conference on Architectural support for programming languages and operating systems. 1996.
Perais, Arthur, and André Seznec. "Practical data value speculation for future high-end processors." 2014 IEEE 20th International Symposium on High Performance Computer Architecture (HPCA). IEEE, 2014.

## Slide 18: Results – Minor CPU
Chart: Predictable Accuracy %
| bzip2 | libquantum | sjeng
LVP_V0 | 0.62351 | 0.0007398 | 0.50977
LVP_V1 | 0.55745 | 0.00014663 | 0.80002
LVP_V2 | 0.41024 | 0.00068648 | 0.40411
LVP_V3 | 0.38367 | 0.00068648 | 0.3818
LVP_V4 | 0.41178 | 0.00068648 | 0.40759
LVP_V5 | 4.5503 | 0.00067981 | 0.81636
LVP_V6 | 0.40955 | 0.00068648 | 0.40539
LVP_V7 | 0.4379 | 0.00010664 | 0.68791
Min: 0.0001, Max: 4.550
Chart: Predictable Coverage %
| bzip2 | libquantum | sjeng
LVP_V0 | 7.3362 | 16.6556 | 0.78255
LVP_V1 | 4.2888 | 0.00025993 | 1.2595
LVP_V2 | 5.7765 | 0.0015996 | 0.6977
LVP_V3 | 5.7 | 0.0015996 | 0.66567
LVP_V4 | 5.775 | 0.0015996 | 0.70186
LVP_V5 | 11.8101 | 0.0015862 | 1.1359
LVP_V6 | 5.771 | 0.0015996 | 0.69898
LVP_V7 | 4.3865 | 0.0002266 | 1.108
Min: 0.0002, Max: 16.66
Notes: % Loads Unpredictable. This is not necessarily an indicator of performance, i.e. libquantum v0 has the lowest % unpredictable, meaning the most are either predictable or constant, but this actually has worse performance in terms of IPC and D$ accesses avoided.

## Slide 19: gem5 Configuration
$GEM5_DIR/build/X86/gem5.opt --outdir=$OUTPUT_DIR $GEM5_DIR/configs/example/se.py --caches --l2cache --cpu-type=DerivO3CPU --l1d_size=32kB --l1i_size=32kB --l2_size=256kB --l3_size=8MB --l1d_assoc=8 --l1i_assoc=8 --l2_assoc=8 --l3_assoc=16 --cpu-clock=3.6GHz -I 20000000

## Slide 20: Implementation – Minor CPU
Decode tags dynamic instructions with prediction classification and value
LSQ modified
  Constant loads are confirmed
  Stores are passed to CVU to invalidate entry
Commit passes loads to LVPT/LCT to update predictions
EarlyMemRef disabled to ensure memory ordering
Fetch 1
Fetch 2
Decode
LVPU
LSQ
GetPrediction
Req
Resp
Const. Load
Store
VerifyPrediction
Issue
Execute
Commit
Notes: Robert
In the minor, we modify the decode stage to tag the dynamic instruction with the load classification and the load value from the LCT and LVPT.
In the commit phase, memory accesses are sent to the LSQ. At the LSQ, for constant loads we check with the CVU to verify that the load can proceed as constant. If it can proceed as constant, the response packet updated with the predicted value and the response is returned without touching the memory hierarchy. All stores are also sent to the CVU to invalidate any matching data addresses to stay coherent with main memory.
Finally, all load instructions that reach commit are sent to the LVP where they strengthen the prediction of LCT and update value of LVPT.

## Slide 21: Implementation
DerivO3 CPU
Fetch
Decode
Rename
I/E/W
LVPU
LSQ
GetPrediction
Req
Resp
Const. Load
Store
VerifyPrediction
Dispatch
Load PC passed to LCT and LVPT during dispatch to get its corresponding prediction.
The load instruction is then pushed into the IQ and LSQ normally.
Once the LSQ starts execution, constant loads are verified. If the prediction is correct, memory access is avoided.
Store addresses are passed to the LVPU once they execute without a fault.
All non-constant loads update the LCT and LVPT after writeback.
Notes: Robert The DerivO3 CPU operates in much the same way. The instruction tagging is done in the Dispatch stage. Instructions are loaded into the Instruction Queue and Load-Store Queue as normal, and the LSQ is similarly modified to verify constant loads. Finally, all loads are sent to the LCT and LVPT for updating in the writeback stage.